## Slide 1
Association Between qPCR Analyses for Oxygenase Enzymes and Rate Constants for Cooxidation of TCE in Groundwater
John T. Wilson (john@scissortailenv.com) and Barbara Wilson
(Scissortail Environmental Solutions, LLC. Ada, OK, USA)
Dora Taggart (dtaggart@microbe.com)
David Freedman (DFREEDM@clemson.edu)

## Slide 2
Methane monooxygenase
SMMO
H-C-OH
H
H
H-C-H
H
H
Phenol monooxygenase
PHE
C
C
C
C
C
C
OH
C
C
C
C
C
C
OH
OH

## Slide 3
Toluene-2-ring monooxygenase
RMO
C
C
C
C
C
C
CH3
C
C
C
C
C
C
CH3
OH
Toluene-2,3-dioxygenase
TOD
C
C
C
C
C
C
CH3
C
C
C
C
C
C
CH3
OH
OH

## Slide 4
Toluene-3-ring monooxygenase
RMO
Toluene-4-ring monooxygenase
RMO
C
C
C
C
C
C
CH3
C
C
C
C
C
C
CH3
OH
C
C
C
C
C
C
CH3
OH
C
C
C
C
C
C
CH3

## Slide 5
Toluene/Xylene Side Chain monooxygenase TOL
C
C
C
C
C
C
CH3
C
C
C
C
C
C
C
O
H

## Slide 6
C=C
H
Cl
Cl
Cl
C
Cl
Cl
H
Cl
C
O
_
TCE
TCE Epoxide
TCE Degradation Products
All these oxygenases cooxidize TCE

## Slide 7
As a first approximation, the relationship between the rate of the cooxidation, the activity of the microorganisms and the concentration of TCE can be described with the Michaelis-Menten Equation.
where: v is the specific rate of the reaction, a zero-order process,
(nmol/(minute*mg cell protein)
S is the concentration of the substrate,
vmax is the maximum rate of the reaction at any value of S,
Km is the Michaelis Constant, (Km = S where v = 0.5 vmax)

## Slide 8
When S << Km, the equation can be simplified to:
and rearranged to:
A first-order rate constant for the reaction is defined as v/S.
When S << Km, then vmax /Km estimates the first-order rate constant.

## Slide 9
Primer | Oxygenase Enzyme | vmax | Km | Km | k
 |  | nmole/ (min· mg protein) | µmole/L | µg/L | L / (year· gene copy)
SMMO | s Methane Monooxygenase | 509 | 145 | 19,053 | 15.6E-08
RDEG | Toluene-2-monooxygenase | 9 | 4 | 526 | 10.0E-08
RMO | Toluene-4-monooxygenase | 20 | 10 | 1,314 | 8.9E-08
TOD | Toluene-2,3-dioxygenase | 8 | 5 | 657 | 7.1E-08
Values for vmax and Km for cooxidation of TCE
Sun and Wood. 1996. Applied Microbiology and Biotechnology 45: 248-256.
Protein in vmax is converted to gene copies in k by assuming the volume of a groundwater bacteria cell is 0.14 (μm)3, the protein content of bacteria is 0.2 g/mL (http://book.bionumbers.org/how-many-proteins-are-in-a-cell/ ) and there is one gene copy per bacteria cell.

## Slide 11
Approach:
Develop an assay for cooxidation of TCE in groundwater using 14C labelled TCE.
Apply the assay at nineteen wells on five sites to extract rate constants for cooxidation of TCE.
Determine the abundance of DNA that was amplified by qPCR probes for oxygenase enzymes.
SMMO + PHE + RDEG + RMO + TOD + TOL
See if (3) can explain (2).

## Slide 12: Clemson Approach: Co-oxidation Analysis Using 14C-TCE
FID
Gas Chromatograph
N2
Packed
Column
4-Port
Valve
Exhaust
Hood
14C-TCE in Acetonitrile (50 µL)
Serum
bottle with GW or FSGW water;
~315 µg/L TCE added along with ~1.1 x 106 dpm 14C

## Slide 13
C=C
H
Cl
Cl
Cl
C
Cl
Cl
H
Cl
C
O
_
TCE
TCE Epoxide
TCE Degradation Products
Volatile
Not Volatile from Alkaline Solution

## Slide 14
Periodically, a small aliquot (3 mL) is taken from the microcosm containing 100 mL of liquid.
The pH of the aliquot is adjusted with base.
The TCE is purged out of the water with a stream of nitrogen.
Then the remaining 14C activity is determined using liquid scintillation counting.
The accumulation of 14C over time is assumed to be degradation products of the TCE.

## Slide 15: Performance Assessment: 14C-TCE Results Tooele Army Depot Well D-20
Production of products from radiolysis of TCE in filter sterilized controls

## Slide 17
Meckenstock et al. 2015., ES&T 49: 7073-7081.
Rate constants may not apply at field scale